## Slide 1: Root-MUSIC, Range, and Doppler Estimations
09/01/2020

## Slide 2: MATLAB Objects and Functions
Phase Array System Toolbox:
  Objects/classes:
    phased.RootMUSICEstimator
    phased.RangeDopplerResponse
    phased.RangeEstimator
    phased.DopplerEstimator
Signal Processing Toolbox
  Function:
    rootmusic()

## Slide 3: phased.RootMUSICEstimator
Multiple Signal Classification DoA Estimation
Properties
  Important:
    SensorArray: ULA (or UCA)
    PropagationSpeed: speed of light or user specified
    OperatingFrequency: central frequency of radar fc
    NumSignalsSource: ‘Property’
    NumSignals: #signal received by ULA (default: 1)
  Others:
    NumSignalsMethod: ‘AIC’ or ‘MDL’ (Akaike Information Criterion or Minimum Description Length Criterion)
    SpatialSmoothing: 0
    ForwardBackwardAveraging: false

## Slide 4: phased.RootMUSICEstimator
H = phased.RootMUSICEstimator()
ANG = H(x)
  For ULA use
  Estimates the direction of arrival (DOA’s) from a signal x
  X is a matrix whose columns correspond to the signal channels.
  ANG is a row vector of estimated broadside angles in degrees.
ANG = H(x, ElAng)
  For UCA use
  ElAng = elevation angles of signals

## Slide 5: Example

## Slide 6: phased.RangeDopplerResponse
Calculate filtered response to range data, perform peak detection, resolve range-Doppler coupling.
Important Properties (for FFT):
  Range Method: FFT
  Signal propagation speed
  Sampling rate
  Sweep slope
  Range FFT Length
  Doppler FFT Length
  Operating Frequency
  Doppler Output: frequency or Speed
[resp,rnggrid,dopgrid] = H(x)
plotResponse(H,x)

## Slide 7: phased.RangeEstimator
Important Properties:
  RMS Resolution
  Noise Power source: ‘input port’ to enable input to step functions
  Cluster Input Port: true to enable input
  Variance output port: true to enable output

## Slide 8: phased.RangerEstimator
H = phased.RangerEstimator()
rngest = H(resp,rnggrid,detidx)
[rngest,rngvar] = H(resp,rnggrid,detidx,noisepower)
[rngest,rngvar] = H(resp,rnggrid,detidx,clusterids)
[rngest,rngvar] = H(resp,rnggrid,detidx,clusterids,noisepower)
rnggrid = units for range dimension of the response data cube
detidx = detection position index

## Slide 9: phased.DopplerEstimator
Important Properties
  Num pulses: number of pulses in doppler-processed waveform
  Noise power source
  Cluster Input port
  Variance output port

## Slide 10: phased.DopplerEstimator
H = phased.DopplerEstimator()
dopest = H(resp,dopgrid,detidx)
[dopest,dopvar] = H(resp,dopgrid,detidx,noisepower)
[dopest,dopvar] = H(resp,dopgrid,detidx,clusterids)
[dopest,dopvar] = H(resp,dopgrid,detidx,noisepower,clusterids)

## Slide 11: Example

## Slide 12: Example

## Slide 13: rootmusic()
w = rootmusic(x,p)
[w,pow] = rootmusic(x,p)
[w,pow] = rootmusic(___,'corr')
[f,pow] = rootmusic(___,fs)
Inputs:
  X = input signal
  P = dimension of signal subspace
  Fs = sampling frequency
Outputs:
  a vector of frequencies, w (rad/sample) or f (Hz)
  and a vector of correspond signal power, pow