## Slide 1: Fast mmWave RF 3D-Object Reconstruction in Low-Visibility Environment via UAV Platform Final Product Presentation 05/14/2021
Team 4
Customer Mentor/Technical Manager:
Dr. Honggang Zhang
Zhuoming Huang(Senior)
Alinson Sanquintin(Junior)

## Slide 2
Technical Manager/ Customer Mentor:
  Dr. Honggang Zhang
Basic team members:
  Zhuoming Huang
    Collects and synthesizes radar and camera sensor data for model training.
    Subsystem tests and analyses.
    Drone development
  Alinson Sanquintin
    Creates CAD models and converts them into point-cloud format.
    Subsystem tests, assists with SAR experiments and data processing.
External team members:
  Yue Sun
    Builds Neural Networks to train AI models and generate 3D radar intensity maps/2D depth images.
  Lucas Lomba
    Helps with PCB design and UAV development
Communication Plan
  Weekly meetings: Zoom
  File sharing: GitHub, Google Drive
  Project management: MS Project
Team Introduction

## Slide 3
Project Management

## Slide 4
Motivations:
Unsafe to access unknown and high-risk areas (smoke, fog, low-visibility) for explorations or rescues [1][2]
Difficult to implement non-intrusive and privacy-preserving monitoring for public health and safety.
Managements of large-scale facilities need plenty of resource (time or labor) in traditional ways.
Application of mmWave radar sensors in autonomous driving.
UAV can move in a 3D space with high efficiency and flexibility.
Problem Definition
Requirements:
Capability to outline the shape of an object in a 3D space
Accurately estimates the position of an object
An UAV platform holding and moving the sensors
Low cost, and simple operations

## Slide 5: System Architecture
Stage 1
Stage 2
Stage 3
Model Training
Ground truth
Full scale 3D intensity maps/2D depth images
Drone
mmWave FMCW
radar sensor
Customized
2D slider
Trained
AI models
2-snapshot 3D intensity maps
Neural Networks
Software
Hardware
Input/
Output
mmWave Studio
MATLAB
FreeCAD
Python
Full-scale 3D intensity maps
Heatmap Generator
Data capture card
Depth camera
Radar sensor configuration
Radar Signal Synthesizer
Point cloud-to-Depth image Generator
CAD models
CAD-to-Point cloud Conversion
2D Depth Images
mmWave FMCW
radar sensor
Real radar signal
Synthesized radar signal
2-snapshot 3D intensity maps
3D physical point cloud
Heatmap Generator
Heatmap Generator
2-snapshot raw data
Full-scale raw data
2-snapshot raw data
64x24
2x24
TI’s IWR6843ISK [3]
TI’s DCA1000EVM [4]
ZED mini [5]

## Slide 6: System Architecture
Stage 1
Stage 2
Stage 3
Model Training
Ground truth
Full scale 3D intensity maps/2D depth images
Drone
mmWave FMCW
radar sensor
Customized
2D slider
Trained
AI models
2-snapshot 3D intensity maps
Neural Networks
Software
Hardware
Input/
Output
mmWave Studio
MATLAB
FreeCAD
Python
Full-scale 3D intensity maps
Heatmap Generator
Data capture card
Depth camera
Radar sensor configuration
Radar Signal Synthesizer
Point cloud-to-Depth image Generator
CAD models
CAD-to-Point cloud Conversion
2D Depth Images
mmWave FMCW
radar sensor
Real radar signal
Synthesized radar signal
2-snapshot 3D intensity maps
3D physical point cloud
Heatmap Generator
Heatmap Generator
2-snapshot raw data
Full-scale raw data
2-snapshot raw data
64x24
2x24
TI’s IWR6843ISK [3]
TI’s DCA1000EVM [4]
ZED mini [5]

## Slide 7: System Architecture
True 2D depth image
Neural Network
Trained AI model
AI-generated 2D depth image
3D radar intensity maps in Cartesian
(2 snapshots)
(full scale)
Reconstructed surface in point cloud
(single view)
Original surface in point cloud (single view)
Reconstruction
Example using CAD car models [1]

## Slide 8: Final Budget
# | Item | Qty | Unit Price | Cost | Description | Status
1 | IWR6843ISK | 1 | $135.00 | $135.00 | mmWave radar sensor | Purchased
2 | ZED mini | 1 | $399.00 | $399.00 | 3D depth camera | Purchased
3 | T6x1-200mm Ball Screw Slide | 4 | $70.00 | $280.00 | For moving the radar sensor horizontally/ vertically in SAR experiments only | Purchased
4 | Arduino Uno | 1 | $23.00 | $23.00 | Slider control | Purchased
5 | Adafruit motor shield | 1 | $19.95 | $19.95 | Motor driver | Purchased
6 | DCA1000EVM | 1 | $499.00 | $499.00 | Raw data capture card, for experiments only | Owned
7 | Customized small 2D sliding mechanism | 1 | N/A | $25 | For forming an SAR on a drone, including 3d-printed parts, timing belts, stepper motors | Purchased
8 | T-slotted rails | 2 | $20.00 | $40.00 | Frame that holds ball screw sliders and radar sensors for SAR experiments | Purchased
9 | OSHPARK PCBs | 1 | $20.80 | $20.80 | Deck connectors | Purchased
10 | Wurth Elektronik FFC connector | 10 | $1.33 | $13.30 | To be used on PCBs | Purchased
11 | Jetson Nano | 1 | $99.00 | $99.00 | Computing unit on drone | Owned
12 | Jetson Nano cooling fan | 1 | $13.70 | $13.70 |  | Purchased
13 | Crazyflie set | 1 | $327.00 | $327.00 | Flight control, including Crazyflie v2.1, BigQuad deck, flow-v2 deck, and multi-ranger deck | Owned
14 | 5V, 2.5A power cable | 1 | $10.00 | $10.00 |  | Purchased
 | Total |  |  | $1714.75 | Data collecting + UAV sensing equipment | 
 | Used budget |  |  | $979.75 | Out of the $1000 budget | 
 | Final product estimated budget |  |  | $965.80 | UAV sensing equipment | 
Pre-owned
Have purchased
Newly added
One time use
Plan to order

## Slide 9: Drone Design
Dimension: 285 x 300 x 160 mm
Weight: 930 g
*Fusion 360

## Slide 10: PCB Design
PCB deck connectors:
A pair of deck connectors with an FFC cable are specifically used to connect the Multi-ranger deck on the top to the other Crazyflie components (e.g., Flow-v2 deck) at the bottom of the drone.
(Measures distance to the ground)
Deck connector A (front/back)
Deck connector B (front/back)
(Measures distance to ceiling and surrounding)
Flexible Flat Cable (FFC)

## Slide 11: PCB Test
Connection test:
Check if FFC connectors are successfully soldered, and if pins are correctly connected.
Result:
Multi-ranger deck is recognized by Crazyflie PC client. No error was reported. All decks are fully functioning together.
https://youtu.be/XsmHnefhABg

## Slide 12: Design Improvements
Larger virtual antenna array size:
  64X8 → 64x24
  Better resolution in azimuth:
Synthesize data using CAD models for model training
  One real data sample takes up to 1 hours for one scenario.
  One synthesized data sample takes about 1.5 minutes for one scenario.
  Speed up data sample collecting process
Matching the coordinate systems of radar 3D intensity maps and camera 2D depth images
  Spherical Coordinates Cartesian Coordinates
64
824

## Slide 13: Design Improvements
2D sliding mechanism for raw data collection
  Manual control Manual/Automatic
  Stable and adjustable with T-slotted rails
UAV platforms
  Mark-I: Controlled by Crazyflie2.1 with BigQuad deck, added Flow-v2 deck for autonomous flights.
  Mark-II: Added Jetson Nano and StereoPi camera, replaced legs.
  Mark-III: Added 2D-sliding mechanism, TI’s IWR6843ISK mmWave radar sensor, multi-ranger deck, replaced StereoPi with ZED mini depth camera.
Mark I (06/2020)
Mark II (08/2020)
Mark III (Developing)

## Slide 14: Ethical Consideration
Privacy Preserving
  Ask for permission if private properties are involved.
  Keep camera off when it is not necessary, or when people feel uncomfortable in front of it.
Safety Standard
  UAV operators must wear protections (safety glasses, cut-resistance gloves)
  Check conditions of motors, propellers, and battery before launching the UAV
  Drop-in net covering the space for flight tests

## Slide 15
Validation
– Depth Camera
Test 1: Depth camera
  Reference: OptiTrack
  In a room with nonuniform light, place markers on the corners, edges, and surfaces of objects (e.g., box, desk). Capture the depth image with depth camera, and record positions of markers with OptiTrack. Measure and compare the distance from depth camera to each marker over 100 frames.
OptiTrack:
A set of fixed optical camera sensors that can provide accurate measurements with positional error < 0.3mm, and rotational error < 0.05°
  *Thank Prof. Rahaim for his OptiTrack system

## Slide 16
Validation Data – Depth Camera
Contrast Brightness | High | Low
High | <1.8% | <11.5%
Low | <5.6% | <21.0%
1. High brightness – High contrast
3. Low brightness – High contrast
2. High brightness – Low contrast
4. Low brightness – Low contrast
Accuracy in distance measurements
Depth
images
Brightness images

## Slide 17
Validation
–mmWave Radar
Test 2: mmWave Radar sensor
  Reference: OptiTrack
  In a room, place objects at some distance. For each object, place markers at the four corners of the surface facing towards the radar sensor. Measure and compare the distance from radar sensor to that surface over 100 frames of video/chirps of signal.
OptiTrack:
A set of fixed optical camera sensors that can provide accurate measurements with positional error < 0.3mm, and rotational error < 0.05°
  *Thank Prof. Rahaim for his OptiTrack system

## Slide 18: Validation Data – mmWave Radar
Antenna array size: 64 x 24
Range resolution ≅ 3.8cm
Elevation angular resolution ≅ 1.8°
Azimuth angular resolution ≅ 4.8°
Distance measurement comparison
 | Metal plate |  | Paper box |  | Foam board | 
 | Diff(cm) | Error | Diff(cm) | Error | Diff(cm) | Error
3m | 1.43 | 0.48% | 3.85 | 1.29% | 5.87 | 1.95%
5m | 1.73 | 0.34% | 4.43 | 0.88% | 7.15 | 1.42%
Tested 3 materials:
  Metal plate: strong reflection
  Paper box: weak reflection
  Foam board: multi-path reflection
Azimuth | Elevation
<16.5% | <4.3%
Angle measurement result

## Slide 19: Validation & Operation
https://youtu.be/aZofhSfoh1s
https://youtu.be/5lDimbV1rhI
Time-lapse SAR operation

## Slide 20
Train | 2475
Verify | 25
Good | 14
Acceptable | 6
Bad | 5
Validation Data – Neural Network
Tested workflow: 2-snapshot 3D radar intensity map → 2D depth image
Generator losses | 
G_GAN: | 0.693
G_L1(*1000): | 2.861
G_Lp(*20): | 21.452
Discriminator losses | 
D_real: | 0.440
D_fake: | 0.693
56%
80%
AI-generated depth images
True depth images (synthesized from CAD car models[1])
Good
Bad
Acceptable
Examples of results:
Matched in color, size and orientation
Similar in color, size and orientation
Wrong size and orientation
Test 3: Neural Network
Synthesized data with CAD car models [1]
Reference: Synthesized 2D depth images
Extract only 2 snapshots of synthesized radar data to generate the 3D intensity maps.
Using 2475 pairs of 3D radar intensity maps and 2D depth images to train an AI model.
Input 25 sets of 3D radar intensity maps to the model, compare the AI generated 2D depth images to synthesized 2D depth images.

## Slide 21
Train | 2500
Verify | 300
Good | 125
Acceptable | 106
Bad | 69
Validation Data – Neural Network
Tested workflow: 2-snapshot 3D radar intensity map → 2D depth image
Generator losses | 
G_GAN: | 0.693
G_L1(*1000): | 26.244
G_Lp(*20): | 21.651
Discriminator losses | 
D_real: | 0.408
D_fake: | 0.694
42%
77%
Test 3: Neural Network
L-shape boxes
Reference: Real + synthesized 2D depth images
400 real data samples + 2400 synthesized data samples
Used 2500 samples for training, 300 for verification
AI-generated depth images
True depth images
Good
Bad
Acceptable
Examples of results:
Matched in color, size and orientation
Similar in color, size and orientation
Wrong color, size and orientation

## Slide 22
Validation Data – Drone
Time (min) | Battery Voltage (V)
0 | 12.53
5 | 12.46
10 | 12.35
15 | 11.72
20 | 11.15
50% Throttle
75% Throttle
100% Throttle
Time (min) | Battery Voltage (V)
0 | 12.51
5 | 12.40
10 | 11.99
15 | 11.16
20 | 10.95
Time (min) | Battery Voltage (V)
0 | 12.60
5 | 11.73
10 | 11.34
15 | 11.13
20 | 9.65
Battery info: 11.1V, 20.0Wh, 1800mAh
Room temperature during tests: 17°C
Tested without running other devices (e.g., Jetson Nano, ZED mini camera, IWR6843ISK radar sensor)
Test 4: Power supply of Drone
  Run the motors under different settings of throttle, record the voltage of battery every 5 minutes.
Sufficient for collecting one data sample (2 snapshots, single point of view),
but insufficient for more data samples or more points of view.

## Slide 23: Example Result
128x128
(size for model training)
1280x720
(original size)
Based on ZED mini configuration (pixel size, focal length, etc.)

## Slide 24: Deliverables
A 3D-object reconstruction system
  Goal: Generates depth images from sparse raw mmWave radar data.
  Data-collecting and model-training
    Raw data collecting mechanism (Fig. 1)
    MATLAB program for generating 3D radar intensity images and 2D depth images.
    Neural networks for training AI Models
  UAV platform design
    Drone with SAR mechanism holding and moving the radar sensor and depth camera (Fig. 2)
Fig. 1
Fig. 2

## Slide 25: Current Status & Future Work
Higher resolution AI-generated depth images → more features for small objects
Deep Neural Network for multiple-view 3D intensity maps/2D depth images
3D-space mapping and reconstruction
Larger loads, longer flight time with bigger drone frame, more powerful motors, and higher capacity battery.
Flight stabilization through better PID tuning and balancing

## Slide 26: Acknowledgement and References
[1] J. Guan, S. Madani, S. Jog, and H Hassanieh.“High Resolution Millimeter Wave Imaging for Self- Driving Cars.”. 2020. IEEE CVPR (2020).
[2] S. Fang and S. Nirjon. “SuperRF: Enhanced 3D RF Representation Using Stationary Low-Cost mmWave Radar.” 2020. International Conference on Embedded Wireless Systems and Networks (EWSN), Vol. 2020. NIH Public Access, 120.
[3] Texas-Instruments, IWR6843ISK, 2021 [Online]. Available: https://www.ti.com/tool/IWR6843ISK
[4] Texas-Instruments, DCA1000EVM, 2021 [Online]. Available: https://www.ti.com/tool/DCA1000EVM
[5] STEREOLABS, ZED mini, 2021 [Online]. Available: https://www.stereolabs.com/zed-mini/
[6] LEYARD, OptiTrack, 2021 [Online]. Available: https://optitrack.com/
Yue Sun: Building Neural Networks
Dr. Honggang Zhang: Customer mentor and technical manager
Dr. Tomas Materdey: Teaching senior design courses
Dr. Michael B. Rahaim: Providing OptiTrack system
Andrew Davis: Supplying resources
Lucas E. Lomba: Helping with drone design

## Slide 27: Thank you
Question?